## Slide 1
Teachable Voice Automation
Teach any Android app once by doing it. Replay it by voice with new values.
Samsung PRISM Gen AI Hackathon | Theme 3
SRM University, Kattankulathur, Chennai | Team Ciphera's
Notes: Open with the one-line pitch: teach once, replay by voice with new parameters, on any app.

## Slide 2
The problem
Voice assistants only work where developers built support.
Per-app integration
Bixby capabilities and app actions need each app's developer to build and maintain them. Most apps never do.
Long tail unserved
Users still tap through the same 6 screens every day in apps that expose no voice API.
Rigid commands
Macro tools replay fixed taps. Change "burger" to "pizza" and they break.

## Slide 3
The solution
Learn by demonstration, generalise with an LLM, replay against the live UI.
1 Teach
Say a command the assistant does not know. Do the task once by hand.
2 Generalise
Groq turns the demo into a flow: steps, selectors, and {{slots}} for the parts that change.
3 Replay
Say it again with new values. The Replayer matches elements on the live screen and acts.
Example: taught "calculate 5 plus 3" -> replayed "what is 9 plus 4" = 13, "compute 6 plus 1" = 7

## Slide 4
Open any app by name
Built in. No demonstration needed.
How it works
The phone sends the backend its launchable apps (label + package). "Open Calculator" is matched on the exact app name and the app is launched.
Safe by construction
Exact-name match only, so "open Bluetooth settings" still replays your taught flow instead of hitting the Settings app. Unknown names fall back to teach mode.
Notes: Answers the first thing a user tries: opening an app. Teaching cannot capture this because launcher taps are ignored by the recorder.

## Slide 5
Architecture
Android does the acting. The backend does the understanding.
Android (Kotlin)
AccessibilityService: read UI tree, tap, type, scroll, back Flow Recorder: events to selectors, passwords redacted Flow Replayer: resourceId > text > desc > class, 6 s wait, retry, LLM fallback Overlay: draggable mic, TEACH MODE indicator, Yes/No Foreground service: push-to-talk audio, WebSocket, TTS playback
Backend (Node, Express, Mongo, Docker)
WebSocket: audio to Deepgram Nova 3 STT Groq JSON mode: intent + slots, generalise, paraphrase match, pick-element fallback Deepgram Aura TTS over the same socket Mongo: Flow + RunLog REST + /dashboard metrics from real RunLogs docker compose up

## Slide 6
Why Accessibility beats app-specific integrations
Per-app integration
One integration per app, built by that app's developer Breaks when the app ships an update they did not plan for Covers only partners
Accessibility + demonstration
Works on apps that know nothing about us The user is the integration: one demo, minutes not months Same UI tree screen readers already use Covers the long tail, including Chrome, Settings, Clock, Calculator

## Slide 7
Demo on a real phone
Realme device, real Accessibility events, real STT and TTS.
Teach mode: user demonstrates
New slot, same flow: 9 + 4 = 13
Confirm before sensitive step

## Slide 8
Measured results
Real phone. Flows and RunLogs reset first. Computed by the dashboard from RunLog data.
Learn success
100%
3 / 3 demonstrations turned into flows
Replay success
100%
9 / 9 replays with new slot values
Paraphrase match
100%
9 / 9 live; 13 / 13 offline eval incl. 2 negative controls
3 flows: Settings, Calculator, Clock. Small sample, own device: read these as a working proof, not a benchmark.
Notes: Be honest: 3 flows, one phone. Two earlier attempts failed while building (slot extraction bug, matcher miss); both fixed and covered by the eval.

## Slide 9
Safety by design
Never auto-complete
Steps that look like pay, send, order, delete are flagged. Replay pauses, speaks "Confirm?", waits for Yes or No. Unclear answer or no answer = No. A declined run is logged as declined, not a failure.
Privacy and secrets
Password / PIN / OTP fields are redacted at record time and never stored or sent to the LLM. Keys only via environment; .env gitignored. Input validated on every endpoint and WebSocket message. Non-root Docker image.

## Slide 10
Limitations, stated plainly
Chrome address-bar suggestion taps emit no accessibility click event, so those flows are hand-authored, not taught.
Long-press and drag gestures are not captured yet.
Operators are not slots: "plus" is baked into the taught calculator flow; "9 minus 4" needs its own demo.
Matching depends on an LLM (openai/gpt-oss-20b on Groq; the Llama model was not available on our key).
Cleartext LAN/localhost transport for development; production needs TLS.
Accessibility must be enabled by the user in Settings; Android does not allow it programmatically.

## Slide 11
Production: an OEM system service
The architecture is what Samsung could ship.
Fallback under Bixby
Bixby stays first choice where a developer built support. Teach mode covers everything else.
On-device
Move STT and the small models on-device. Flows stay private on the phone.
System-level trust
As a privileged service: signed confirmations, per-app policy, shareable flows.